## Slide 1: Inženjerstvo softvera za Internet-Web of Things
Komunikacija

## Slide 2: Uvod
Ključni delovi IoT tehnologije su:
  Senzori
  Aktuatori
  Komunikacija
Komunikacija je omogućena upotrebom velikog broja tehnologija:
  Bluetooth
  WiFi
  NFC (Near Field Communication)
  RFID (Radio Frequency Identification)
  Zigbee
  LoRa (Long Range)
  Ethernet,...

## Slide 3: Protokoli
Obradićemo
  TCP/IP protokol
    WiFi
    Ethernet
  Bluetooth Low Energy (BLE)

## Slide 4: TCP/IP

## Slide 5: Osnovne odrednice TCP/IP protokola
Osnova je IP mrežni protokol
Pojam socket-a: par (IP adresa, port)
Mogućnost korišćenja TCP i UDP protokola
  Razlika

## Slide 6: Socket 1/2
Par (IP adresa, port)
Uspostavljena veza između dva programa određena je parom socket-a

## Slide 7: Socket 2/2
Više programa u vezi

## Slide 8: Identifikacija čvorova mreže
Pomoću simboličke adrese, npr. www.yahoo.com
  DNS
Pomoću numeričke adrese, podeljene u oktete, npr. 147.91.177.196
IPv4 vs. IPV6

## Slide 9: TCP/IP server u Pajtonu
s = socket.socket() # Create a socket object
print ('Waiting for connections on host: ' + host)
s.bind((host, port)) # Bind to the port
s.listen(5) # Now wait for client connection.
while True:
c, addr = s.accept() # Establish connection with client.
print ('Got connection from ', addr)
threading.Thread(target=threadsock, args=[c]).start()

## Slide 10: TCP/IP server u Pajtonu
def threadsock(c):
# kada se neko spoji na nas program preko socketa
# procitamo maks 1KB od klijenta
text = c.recv(1024)
if text == b'':
return
print (text)
# pristupicemo globalnoj promenljivoj counter da bismo je menjali
global counter
counter = counter + 1
text = 'counter: ' + str(counter) + '\n'
c.send(text.encode())
c.close()

## Slide 11: TCP/IP klijent u Pajtonu
client_socket = socket.socket() # instantiate
print ('Connecting to: ' + host)
client_socket.connect((host, port)) # connect to the server
message = input(" -> ") # take input
client_socket.send(message.encode()) # send message
data = client_socket.recv(1024).decode() # receive response
print('Received from server: ' + data) # show in terminal
client_socket.close() # close the connection

## Slide 12: REST klijent u Pajtonu
Koristimo, recimo, Requests biblioteku
import requests
requests.get(STATUS_HOST)
requests.get(STATUS_HOST, timeout=0.1)

## Slide 13: TCP/IP komunikacija na Arduino/ESP32
Nema operativnog sistema
  Koriste se biblioteke
Biblioteke za WiFi i za Ethernet
  Podrška za WiFi je ugrađena u postojeće biblioteke
  Podrška za Ethernet zavisi od hardvera i mora da se instalira

## Slide 14: TCP/IP server preko WiFi na ESP32
void handleRoot() {
server.send(200, "text/plain", "hello from esp8266!");
}
void handleNotFound() {
server.send(404, "text/plain", "not found");
}
void setup(void) {
WiFi.begin(ssid, password);
while (WiFi.status() != WL_CONNECTED) { delay(500); }
server.on("/", handleRoot);
server.on("/inline", []() {
server.send(200, "text/plain", "this works as well");
});
server.onNotFound(handleNotFound);
server.begin();
}
void loop(void) {
server.handleClient();
}
const char* ssid = "........";
const char* password = "........";
WebServer server(80);

## Slide 15: TCP/IP klijent preko WiFi na ESP32
void setup(void) {
WiFi.begin(ssid, password);
while (WiFi.status() != WL_CONNECTED) { // Wait for connection
delay(500);
}
HTTPClient http;
http.begin("http://neki.server.com/putanja");
int httpCode = http.GET();
if(httpCode > 0) {
if(httpCode == HTTP_CODE_OK) {
String payload = http.getString();
}
}
http.end()
}

## Slide 16: Skeniranje WiFi
void setup() {
Serial.begin(115200);
// Set WiFi to station mode and disconnect from an AP if it was previously connected
WiFi.mode(WIFI_STA);
WiFi.disconnect();
delay(100);
}
void loop() {
Serial.println("scan start");
// WiFi.scanNetworks will return the number of networks found
int n = WiFi.scanNetworks();
if (n > 0) {
for (int i = 0; i < n; ++i) {
Serial.printf("%s (%s) ", WiFi.SSID(i), WiFi.RSSI(i));
Serial.println((WiFi.encryptionType(i) == WIFI_AUTH_OPEN)?" ":"*");
delay(10);
}
}
delay(5000);
}

## Slide 17: TCP/IP preko Etherneta na ESP32 i RPI Zero
Nema ugrađen Ethernet port
Mora da se nabavi
Jevtino Ethernet rešenje: ENC28J60 modul
  za njegov rad je potreban SPI interfejs, a to svi navedeni uređaji poseduju (za RPI Zero W je samo potrebno da se uključi podrška za SPI u okviru raspi-config aplikacije)
Repozitorijumi:
  Arduino: https://github.com/njh/EtherCard
  https://github.com/UIPEthernet/UIPEthernet
  RPI: https://mvidakovic.blogspot.com/2018/08/raspberry-pi-stuff.html#zeroeth

## Slide 18: ENC28J60 modul

## Slide 19: ENC28J60 na RPI
Pi PinNo ENC28J60
-----------------------------------
+3V3 17 VCC
GPIO10/MOSI 19 SI
GPIO9/MISO 21 SO
GPIO11/SCLK 23 SCK
GND 20 GND
GPIO25 22 INT
GPIO8/CE0 24 CS
Dodati u /boot/config.txt
dtoverlay=enc28j60

## Slide 20: TCP/IP server na ENC28J60
EthernetServer server = EthernetServer(LISTENPORT);
void setup() {
uint8_t mac[6] = {MACADDRESS}; uint8_t myIP[4] = {MYIPADDR}; uint8_t myMASK[4] = {MYIPMASK};
uint8_t myDNS[4] = {MYDNS}; uint8_t myGW[4] = {MYGW};
Ethernet.begin(mac, myIP, myDNS, myGW, myMASK);
server.begin();
}
void loop() {
while(true) {
size_t size;
if (EthernetClient client = server.available()) {
while((size = client.available()) > 0) {
uint8_t* msg = (uint8_t*)malloc(size+1); memset(msg, 0, size+1);
size = client.read(msg,size);
printf(msg); // uradimo nešto sa primljenom porukom
free(msg);
}
client.stop();
}
}

## Slide 21: TCP/IP klijent na ENC28J60
EthernetClient client;
void setup() {
uint8_t mac[6] = {MACADDRESS}; uint8_t myIP[4] = {MYIPADDR};
uint8_t myMASK[4] = {MYIPMASK}; uint8_t myDNS[4] = {MYDNS};
uint8_t myGW[4] = {MYGW};
Ethernet.begin(mac, myIP, myDNS, myGW, myMASK);
}
void loop() {
if (client.connect(server_addr, PORT)) {
client.printf("GET /level/%d/DEVICE%d HTTP/1.1\r\nHost: %s:5000\r\n\r\n", lightValue, DEVICE_ID, myIPAddress);
Serial.printf("Available bytes: %d\n", client.available());
client.flush();
usleep(100000); // 0.1 sec sleep
client.stop();
return;
}
}

## Slide 22: Rad sa HTTPS na Arduino/ESP32 platformi
Nije automatski podržana
  Nedovoljno resursa da se implementira provera HTTPS sertifikata preko CA (Certificate Authority)
Sertifikat mora da se ugradi u kod
  Prvo se pokupi sa web sajta
  Iskonvertuje se u niz bajtova
  Ugradi u kod
  Komplikovano, zar ne?

## Slide 23: Bluetooth Low Energy

## Slide 24: Bluetooth
Bežična komunikaciona tehnologija kratkog dometa
Opseg frekvencija: 2,402GHz do 2,48GHz
Osnovna namena je bila da zameni žične konekcije za razmenu datoteka između računara i mobilnih telefona, kao i da zameni žične slušalice
  To se proširilo na:
    Bežične slušalice, zvučnike i mikrofone
    Bežične miševe i tastature
    Bežične selfie stick-ove
    Praćenje lokacije uređaja i objekata
    Ostalo

## Slide 25: Bluetoothe Low Energy (BLE)
Omogućava bežični prenos podataka između "low energy" uređaja (beacons) i ostalih uređaja
Ideja je da beacon periodično šalje Advertizing poruke, koje ostali uređaji (smartphones) mogu da primete i da se konektuju na beacone
Namena:
  Pametni satovi (smart watches)
  Bežični monitori zdravstvenih parametara
  Fitness trackers
  Bežične slušalice, mikrofoni, itd.
  HID (Human Interface Device) devices (bežične tastature, miševi, itd.)
  Ostalo

## Slide 26: Osnove BLE
Radi na opsegu frekvencija od 2.400GHz do 2.4835 GHz
Koristi se Generic Attribute Profile (GATT):
  Client – uređaj koji se spaja na beacon, na primer pametni telefon
  Server – uređaj na koji se spajaju klijenti, na primer fitness tracker
  Characteristic (karakteristika) – vrednost koja se prenosi od beacona do uređaja, na primer, napon na bateriji
  Service (servis) – kolekcija karakteristika koje podržava beacon
  Descriptor (opis) – dodatne informacije o karakteristici, na primer, jedinica mere (Volt)
  Identifiers – karakteristike, servisi i opisi se identifikuju jedinistvenim identifikatorom - UUID

## Slide 27: BLE na RPI
Modeli koji imaju WiFi, imaju i BLE
Postoje razne biblioteke koje se mogu koristiti za BLE
  bleak: pip install bleak
Skeniranje BLE uređaja u blizini:
import asyncio
from bleak import BleakScanner
async def main():
devices = await BleakScanner.discover()
for d in devices:
print(d)
asyncio.run(main())

## Slide 28: BLE advertisment data
devices = await BleakScanner.discover(
return_adv=True, cb=dict(use_bdaddr=args.macos_use_bdaddr)
)
for d, a in devices.values():
print(d)
print(a)

## Slide 29: Prijem notifikacija sa BLE uređaja
def match_nus_uuid(device: BLEDevice, adv: AdvertisementData):
print(adv.local_name)
if adv.local_name == 'ESP32 UART Test':
return True
return False
device = await BleakScanner.find_device_by_filter(match_nus_uuid)
def handle_rx(_: BleakGATTCharacteristic, data: bytearray):
print("received:", data)
async with BleakClient(device, disconnected_callback=handle_disconnect) as client:
await client.start_notify(UART_TX_CHAR_UUID, handle_rx)

## Slide 30: Slanje podataka od RPI na BLE uređaj
nus = client.services.get_service(UART_SERVICE_UUID)
rx_char = nus.get_characteristic(UART_RX_CHAR_UUID)
s = "sadfasdf"
client.write_gatt_char(rx_char, s)

## Slide 31: BLE uređaj na ESP32
ESP32 može da radi kao BLE uređaj
Inicijalizacija:
#define SERVICE_UUID "6E400001-B5A3-F393-E0A9-E50E24DCCA9E" // Nordic UART Service UUID
#define CHARACTERISTIC_UUID_RX "6E400002-B5A3-F393-E0A9-E50E24DCCA9E"
#define CHARACTERISTIC_UUID_TX "6E400003-B5A3-F393-E0A9-E50E24DCCA9E"
// Create the BLE Device
BLEDevice::init("ESP32 UART Test"); // Give it a name
// Create the BLE Server
BLEServer *pServer = BLEDevice::createServer();
pServer->setCallbacks(new MyServerCallbacks());
// Create the BLE Service
BLEService *pService = pServer->createService(SERVICE_UUID);
// Create a BLE Characteristic
pCharacteristic = pService->createCharacteristic(
CHARACTERISTIC_UUID_TX,
BLECharacteristic::PROPERTY_NOTIFY
);
pCharacteristic->addDescriptor(new BLE2902()); // Karakteristika za notifikacije mora da ima deskriptor (0x2902)
Client Characteristic Configuration

## Slide 32: Callback kada se neko spoji na ESP32
class MyServerCallbacks: public BLEServerCallbacks {
void onConnect(BLEServer* pServer) {
deviceConnected = true;
digitalWrite(LED, HIGH);
#ifdef DEBUG
Serial.println("Device connected");
#endif
};
void onDisconnect(BLEServer* pServer) {
deviceConnected = false;
digitalWrite(LED, LOW);
#ifdef DEBUG
Serial.println("Device disconnected");
#endif
ESP.restart(); // ponekad upadne u čudno stanje nakon raskida BLE veze, pa ga restartujemo
}
};

## Slide 33: Nastavak inicijalizacije – registracija prijema poruka od uređaja
BLECharacteristic *pCharacteristic2 = pService->createCharacteristic(
CHARACTERISTIC_UUID_RX,
BLECharacteristic::PROPERTY_WRITE
);
pCharacteristic2->setCallbacks(new MyCallbacks());
// Start the service
pService->start();
// Start advertising
pServer->getAdvertising()->start();
#ifdef DEBUG
Serial.println("Waiting a client connection to notify...");
#endif

## Slide 34: Callback za prijem poruka od uređaja
class MyCallbacks: public BLECharacteristicCallbacks {
void onWrite(BLECharacteristic *pCharacteristic) {
std::string rxValue = pCharacteristic->getValue();
if (rxValue.length() > 0) {
Serial.print("Received Value: ");
for (int i = 0; i < rxValue.length(); i++) {
Serial.print(rxValue[i]);
}
// Do stuff based on the command received from the app
if (rxValue.find("A") != -1) {
Serial.print("Turning ON!");
digitalWrite(LED, HIGH);
}
else if (rxValue.find("B") != -1) {
Serial.print("Turning OFF!");
digitalWrite(LED, LOW);
}
}
}
};