## Slide 1: Inženjerstvo softvera za Internet-Web of Things
Asinhrona razmena poruka

## Slide 2: Uvod
Komunikacija je ključni deo IoT steka
Videli smo da možemo lako da uspostavimo vezu između dva i više elementa IoT
  Bazirano uglavnom na TCP/IP protokolu
Messaging (asinhrona razmena poruka) je viši nivo apstrakcije, koji omogućuje ono što mu ime kaže
  Asinhrona Razmena Poruka
Ideja je da učesnici u komunikaciji mogu da asinhrono, pouzdano i sigurno razmenjuju poruke
  Više prijemnika/predajnika

## Slide 3: Messaging Systems
Asinhrono
  Nonblocking request processing
Pouzdano
  Garantovana isporuka čak i ako primalac ne radi (perzistencija poruka)
Sigurno
  Enkripcija
Program
Messaging
System
Program

## Slide 4: Dva načina rada
Publish/subscribe
Point-to-point

## Slide 5: Publish/subscribe
Više predajnika i prijemnika podešenih na jedan "kanal"

## Slide 6: Point-to-point
Omogućava komunikaciju između dva učesnika posredstvom reda (Queue)
Svaka poruka u redu se tačno jednom upotrebi
Može i više predajnika i prijemnika ali gornje ograničenje i dalje postoji

## Slide 7: Messaging Protokoli
Više protokola
  MQTT (Message Queue Telemetry Transport)
  AMQP (Advanced Message Queue Protocol)
  XMPP (Extensible Messaging and Presence Protocol)
  DDS (Data Distributed Service)
  ...

## Slide 8: MQTT

## Slide 9: MQTT (Message Queue Telemetry Transport)
Bazira se na klijent/server arhitekturi
  Server se zove broker
Podržava publish/subscribe način rada
Tri nivoa pouzdanosti:
  Nikakav – poruke se ne čuvaju
    Ako je neko od učesnika offline, neće dobiti poruku
  Queued persistent – poruke se čuvaju u memoriji (queue)
    Klijenti ne moraju da budu online da bi primili poruku
  Persistent with acknowledgment – klijent mora da potvrdi prijem, inače će mu poruka biti isporučena ponovo

## Slide 10: MQTT (Message Queue Telemetry Transport)
Sigurnost:
  Enkripcija
  Autentikacija
  Autorizacija

## Slide 11: MQTT na RPI
Mosquitto broker
sudo apt-get install mosquitto -y
sudo apt-get install mosquitto-clients –y
Konfiguracija u /etc/mosquito/mosquito.conf:
...
#include_dir /etc/mosquitto/conf.d
allow_anonymous false
password_file /etc/mosquitto/pwfile
listener 1883

## Slide 12: MQTT na RPI
Dodavanje korisnika:
sudo mosquitto_passwd -c /etc/mosquitto/pwfile mqtt
Testiranje pretplate (subscribe):
mosquitto_sub -h addr -d -u mqtt -P mqtt -t test
Testiranje slanja poruke (publish):
mosquitto_pub -h addr -d -u mqtt -P mqtt -t test -m "HELLO"
Paho client za MQTT:
pip install paho-mqtt

## Slide 13: MQTT na RPI u Pajtonu
client = mqtt.Client()
client.on_connect = on_connect
client.on_message = on_message
client.username_pw_set("mqtt", "mqtt")
client.connect("192.268.137.110", 1883, 60)
client.publish("test", "Once from client")
# Blocking call that processes network traffic, dispatches callbacks and
# handles reconnecting.
# Other loop*() functions are available that give a threaded interface and a
# manual interface.
client.loop_forever()
Ako imamo username/password, a ovo ne napišemo, neće prijaviti grešku, već neće primati poruke

## Slide 14: MQTT na RPI u Pajtonu - callbacks
# Callback for when the client receives a CONNACK response from the server.
def on_connect(client, userdata, flags, rc):
print("Connected with result code "+str(rc))
# Subscribing in on_connect() means that if we lose the connection and
# reconnect then subscriptions will be renewed.
client.subscribe("test")
# The callback for when a PUBLISH message is received from the server.
def on_message(client, userdata, msg):
print(msg.topic+" "+str(msg.payload))

## Slide 15: MQTT na Arduino/ESP32
Biblioteka PubSubClient
  https://github.com/knolleary/pubsubclient
Potrebno je da mikrokontroler spojimo na mrežu ili preko WiFi, ili preko Etherneta
Može i da objavljuje (publish) i da prima (subscribe) poruke preko teme (topic)

## Slide 16: MQTT na Arduino/ESP32 - inicijalizacija
// WiFi
const char *ssid = "SSID"; // Enter your Wi-Fi name
const char *password = "SIFRA"; // Enter Wi-Fi password
// MQTT Broker
const char *mqtt_broker = "192.168.137.1";
const char *topic = "test";
const char *mqtt_username = "mqtt";
const char *mqtt_password = "mqtt";
const int mqtt_port = 1883;
WiFiClient espClient;
PubSubClient client(espClient);

## Slide 17: MQTT na Arduino/ESP32 - inicijalizacija
void setup() {
client.setServer(mqtt_broker, mqtt_port);
client.setCallback(callback);
while (!client.connected()) {
String client_id = "esp32-client-";
client_id += String(WiFi.macAddress());
Serial.printf("The client %s connects to the MQTT broker\n", client_id.c_str());
if (client.connect(client_id.c_str(), mqtt_username, mqtt_password)) {
Serial.println("Connected to broker.");
} else {
Serial.printf("Failed with state %d\n", client.state()); delay(2000);
}
}
// Publish and subscribe
client.publish(topic, "Hi, I'm ESP32");
client.subscribe(topic);
}

## Slide 18: MQTT na Arduino/ESP32 - callback
void callback(char *topic, byte *payload, unsigned int length) {
Serial.print("Message arrived in topic: ");
Serial.println(topic);
Serial.print("Message:");
for (int i = 0; i < length; i++) {
Serial.print((char) payload[i]);
}
Serial.println();
Serial.println("-----------------------");
}

## Slide 19: Zaključak
Jednostavne, proverene implementacije za razmenu poruka
Jednostavan asinhroni (neblokirajući) prijem poruka
Jednostavno slanje poruka
Zahteva instalaciju Messaging servera (brokera) na RPI i/ili dalje